## Slide 1
Comparison of Multi-Channel EEG Based Graph Learning Methods
Dr. Mohammad B. Shamsollahi
Arshak Rezvani
#WomanLifeLiberty

## Slide 2: Hello!
I am Arshak Rezvani
I am here because I love to give presentations.
You can find me at @ArshakRz

## Slide 3: What is Multi-Channel EEG Signals? [1]
Electrode placement systems.
  The 10-20 System of Electrode Placement
Electroencephalogram Time Series and Channels.
Like Noise!

## Slide 4: Pre-Processing [1]
Artifact Rejection
    Physiologic
      EMG
      ECG
      EOG
      Blinking
      Sweat
    Non-Physiologic
      AC electrical and electromagnetic interferences
      Electrode pop and Movement

## Slide 5: EEG as a Random Process [1]
Ergodicity
  Mean Ergodic
  Correlation Ergodic
Averaging between trials
  Cause indeterministic

## Slide 6: But What is a Graph Signal? [2]
A Graph!
  Adjacency Matrix
  Laplacian Matrix
Graph Signal
  Definition and Example
    It’s a Domain
      Time
      Frequency
      Vertices
    No Order!
      A Vector

## Slide 7: Graph Operations [2]
Graph Shift
  Multiplication by Laplacian Matrix
    Shift with weights like time series
Graph Fourier Transform(GDFT)
  Linear Shift Invariant Systems(LSI)
  Eigen Function
    for time series
    Eigen Vectors of Laplacian Matrix
Graph Filtering and Convolution
Sampling Over Graphs
Graph Wavelet Transform
Initial Signal
Shifted Signal

## Slide 8: Graph Learning [3]
Estimating Functional Connectivity
  Connectivity Measures
    Regression Methods
      Pearson Correlation
      The Magnitude-Squared Coherence Function

## Slide 9: Graph Learning [3]
Estimating Functional Connectivity
  Connectivity Measures
    Phase Synchronization Methods
      Using Hilbert Transform:
      Using Wavelet Transform:
      Getting Mod.
      Shannon Entropy
      Mean Phase Coherence

## Slide 10: Very Complex Laplacian Matrix

## Slide 11: How To Make It Less Complex [4]
Fail to Represent Discriminative Patterns
  Graphs vary significantly in different subjects
Common Edge Graph

## Slide 12: CEG(Common Edge Graph) [4]
Frequency Bands
Compute Correlation and Coherence
Define a graph with the M most similar edges
  Sorts The Edges of The Complete Graph
    Where
    Nodes:
    Edges:
    The CEG is defined with same nodes and
    Edges:

## Slide 13: Results [4]

## Slide 14: Learning Graphs From A Smooth Signal
Not Using the smoothness and time series properties
Learning the Laplacian as a whole

## Slide 15: Smoothness On a Graph Definition [5]
How to quantify how smooth a set of vectors are on a given weighted undirected graph?
Vectors: so we have
Smoothness on the Graph:
The Optimization Problem:

## Slide 16: Pairwise Distance Matrix [5]
Definition:
Some math:
The smoothness term is a weighted -1 norm of W, encoding weighted sparsity.
But…

## Slide 17: Building a Sparse Laplacian [5]
We Explicitly add a sparsity term:
It is free!
All info. about signal(X) is in Z and we have the sparsity.
So we can use any connectivity measures(Pairwise Distance)

## Slide 18: Other Constraint [5]
Make sure that each node has at least one edge with another node
And control sparsity
New Optimization Problem:
  The log controls node degree vector(No zero or negative degrees)
  However, log makes it very sparse
    Can not use the technique before
    So we use Frobenius Norm

## Slide 19: Convex Optimization [5][6]
Blah, Blah, Blah

## Slide 20: Testing Criteria[8][9]
Accuracy of a Classifier
  SVM
  Neural Network
  Decision Tree
  Etc.

## Slide 21: Graph Features [10]
Laplacian Matrix Elements
Two Norm Total Variation of Eigen Vector(TNTV)
Graph Laplacian Energy (GLE)
D = 2E/M, E is number of edges and M being the number of nodes of graph.
Joint Total Variation Energy (JTVE)

## Slide 22: Graph Features
Much more! [7][8]
  Degree: number of links connected to a node
  Shortest path length: a basis for measuring integration
  Global efficiency
  Transitivity
  Participation coefficient
  Average neighbor degree
  Etc.
PCA and Dimensionality Reduction!

## Slide 23: References
Hajipour Sardouie, Sepideh. " EEG Signal Processing Course Notes." Sharif University of Technology(2022). [1]
Amini, Arash A. " Graph Signal Processing Course Notes." Sharif University of Technology(2021). [2]
Wendling, Fabrice, et al. "From EEG signals to brain connectivity: a model-based evaluation of interdependence measures." Journal of neuroscience methods 183.1 (2009): 9-18. [3]
López, Rafae Lemuz, et al. "Graph theory for brain connectivity characterization from EEG." 2020 10th International Symposium on Signal, Image, Video and Communications (ISIVC). IEEE, 2021. [4]
Kalofolias, Vassilis. "How to learn a graph from smooth signals." Artificial Intelligence and Statistics. PMLR, 2016. [5]
Kalofolias, Vassilis, and Nathanaël Perraudin. "Large scale graph learning from smooth signals." arXiv preprint arXiv:1710.05654 (2017). [6]
Rubinov, Mikail, and Olaf Sporns. "Complex network measures of brain connectivity: uses and interpretations." Neuroimage 52.3 (2010): 1059-1069. [7]
Sen, Bhaskar, et al. "Classification of obsessive-compulsive disorder from resting-state fMRI." 2016 38th Annual International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC). IEEE, 2016. [8]
Saboksayr, Seyed Saman, Gonzalo Mateos, and Mujdat Cetin. "EEG-based emotion classification using graph signal processing." ICASSP 2021-2021 IEEE International Conference on Acoustics, Speech and Signal Processing (ICASSP). IEEE, 2021. [9]
Mathur, Priyanka, and Vijay Kumar Chakka. "Graph Signal Processing Based Cross-Subject Mental Task Classification Using Multi-Channel EEG Signals." IEEE Sensors Journal 22.8 (2022): 7971-7978. [10]

## Slide 24
Thanks for Your Attention!